# The Antonín Dvořák Theatre

# Technical data

## Distance between portal  8,73 m

## Distance from the centre of the turntable to the iron  5,89 m

## Distance from the orchestra pit edge to the turntable edge  2,20 m

Distance from the iron to the turntable edge 1,44 m

Distance from the iron to the portal edge  1,08 m

Distance from the orchestra pit edge to the iron  0,58 m

turntable – diameter 8,86 m

traps on the turntable  2 pc – 99 x 99 cm , in the turntable axis , from the centre of turntable 1 – 188,5 cm, 2 – 184,5 cm

electric clatters on the turntable  on the turntable  - 2 pieces / sockets

orchestra pit in the axis 3,25 m ,vehicles – 3 pieces ,

orchestra pit  depth- 2,26 m ,step 19,5 cm

orchestra pit  parapet, width  43 cm + step width 25 cm,height16,5 cm/13,5 cm

orchestra pit  parapet  - auditorium/ – 87 cm + 17 cm step

stage depth from wall to wall   11 m

stage depth from screen to screen  14,88 m

distance from the right portal to screen  3,10 m, to wall 3,80 m

distance to portal 1bar55 cm

iron curtain width  13 cm

tin portal - height 5,53 m ,  5,52,5 m ,  width 70 cm

bridge left portal+ 2,21 m/ under + 2,06 m

air-conditioning  –  height – from the stage floor – 2,65 m

width left side  - side and rest  – 45 cm

right side rest 45 cm, side 20 cm

prospect clatters 10,88 x 0,68 m

manual bar average  6 cm – length 9,40 m, 14 pieces , telescopes  40 cm, lifting capacity 80 kg

motor bar profile 60 x 40 mm – lenght  9,40 m,13  pieces , telescopes 40 cm, lifting capacity  240 kg

bar range: 	main stage 16,15 m

rear stage M 4,83 m , manual 5,23 m

bridges HJ – 1.  – 6,79 m  ,  2.  – 11,38 m  , 3. 15,08 m railing height 1,10 m

ZJ  - 3,33 m railing 1,15 m

Booth ceiling – height 4,21 m

Carriage route decoration warehouse  – height – profile  I  from the ground 3,20, hooks from the ground  2,20 m

Stairs leading to decoration warehouse  – 13 x  14/35 cm

## Distance between bars – main stage:

Right side  							left side

wall - 1		225 cm

1-M1            		25 cm

M1- 2			25 cm

2 - M2            	25 cm

M2 - M4          	176 cm			wall – 3         		327 cm

3 – M3		25 cm

M3 – 4		45 cm

4 – RAMP		45 cm

M4 – 5		25 cm

5 - M5			25 cm

M5 - 6			25 cm

6 - M6			25 cm

M6 – 7		25 cm

7 - RAMP		50 cm

RAMP – M7	40 cm

M7 - 8			18 cm

8 - M8			40 cm

M8 – 9		25 cm

9 - M9			25 cm

M9 – 10		25 cm

10 - M10		25 cm

M10 - 11		25 cm

11- RAMP		50 cm

RAMP – 12		45 cm

12 - M11		25 cm

M11 – 13		25 cm

13 - M12		25 cm

M12 – 14		25 cm

14 - M13		25 cm

M13 – wall 		20 cm

## Distance between bars – rear stage:

From alcove - 15	68 cm

15  -  16		25 cm

16  -  17		25 cm

17  -  18		25 cm

18  -  19		25 cm

19  -  20		66 cm

20  -  21		25 cm

21  -  22		25 cm

22  -  23		25 cm

23  -  24		25 cm

24  -  25		25 cm

25  -  26		25 cm

# 26  -  27		25 cm

27  -  28		25 cm

28  -  29		40 cm

29  -  30		78 cm

## Stage technology

| Equipment: | Maximum load: |
| --- | --- |
| Orchestra pit lifts S1 – S3 | 500 kg/m2 static 100 kg/m2 dynamic 1 500 kg overall |
| Stage motor trap V1 – V2 | 200 kg |
| Manual stage bars 1 – 13 | 80 kg |
| Horizontal manual bar 14/H1 | 90/60 kg |
| Manual stage bars – rear stage 15 – 30 | 80 kg |
| Motorised stage bars M1 – M13 | 240 kg |
| Motorised stage bars - rear stageM14 – M16 | 160 kg |
| Prospect bar – rear stage M17 | 160 kg |
| Fire curtain Z1 (weight) | 3 800 kg |
| Main curtain F1 | 85/60 kg |
| Bobbinet bar N1 | 160 kg |
| Lighting battery - underbridge BI | 90/80 kg |
| Lighting battery BII – BIV | 150/150 kg |
| Blocking wraps – lift light E1 | 70/80 kg |
| Blocking wraps – lift rightE2 | 70/80 kg |
| Telescopic hangers of lights left C1 – C4 | 15 kg |
| Telescopic hangers of lights right C4 – C8 | 15 kg |
| Turntable - main stage ø 9 m | 300 kg/m2 |